## Slide 1
SCIML PROJECT
PRESENTATION
Presented By:
Aditya Prasad
ME 4th year Undergraduate Student
18th Nov, 2025

## Slide 2
ChemNODE-Ammonia: A Neural ODE Surrogate for Stiff Ammonia-Air Combustion Kinetics
01
Some Basic Questions
What's the Problem?
  A 3D simulation (like a flame) is a grid of millions of tiny "boxes" or cells.
  The slowest part of the simulation (>90% of CPU time) is solving the complex chemical reactions in every single box.
What is 0D Combustion?
  A 0D model is a single "perfectly stirred" box.
  It's where we solve the fundamental problem: How do chemicals change over time?
Our Project's Goal:
  By building a super-fast Neural Network to solve the 0D problem, we can create a "surrogate" to accelerate the entire 3D simulation.

## Slide 3
02
INTRODUCTION & MOTIVATION
What is the problem?
  Ammonia (NH3) is a promising carbon-free fuel, essential for decarbonizing sectors like power generation and shipping.
  Accurately simulating ammonia combustion is vital for designing efficient, low-NOx engines and turbines.
What is the computational bottleneck?
  DETAILED CHEmical mechanisms (e.g., Stagni (2023): 31 species, 203 reactions) are computationally prohibitive.
  The problem is "Numerical Stiffness": The system has a massive range of timescales (e.g., fast radicals vs. slow N2 formation).
  Stiff solvers (like Cantera's default) must take tiny, slow, and expensive time steps to remain stable.

## Slide 4
03
PROBLEM STATEMENT & OBJECTIVES
01
03
02
OBJECTIVE
TO DEVELOP A COMPUTATIONALLY-EFFICIENT SURROGATE MODEL THAT ACCURATELY REPRODUCES THE STIFF AMMONIA KINETICS.
PROBLEM STATEMENT
THE NUMERICAL STIFFNESS OF THE 31-SPECIES AMMONIA MECHANISM MAKES IT COMPUTATIONALLY INTRACTABLE TO COUPLE WITH MULTI-DIMENSIONAL CFD SIMULATIONS.
SPECIFIC GOALS
  ACCURACY: THE SURROGATE MUST ACCURATELY PREDICT THE FULL TIME-EVOLUTION OF SPECIES AND TEMPERATURE FOR UNSEEN INITIAL CONDITIONS (T0 & PHI).
  Speed: The surrogate must reduce the numerical stiffness, enabling it to be integrated by a fast, explicit ODE solver (like dopri5) and achieve a significant speed-up over the original stiff solver.

## Slide 5
Project.
04
LITERATURE SURVEY / BACKGROUND
From ResNets to Neural ODEs (NODEs):
  A standard ResNet is essentially a discrete-time model (like an Euler-step).
  A Neural ODE (Chen et al., 2018) is the continuous-time limit, parameterizing the derivative dh/dt = f(h, t, theta) with a single network.
  Key Benefit: It uses the Adjoint Sensitivity Method for backpropagation, achieving a constant O(1) memory cost (unlike ResNets, which are O(L) ).
NODEs for Chemistry (ChemNODE):
  The "ChemNODE" framework (Owoyele & Pal, 2022) applies this to chemical kinetics, where the network f learns the chemical source term.
The Critical Challenge: Stability:
  Bansude et al. (2023) noted that training NODEs on stiff, multi-scale chemistry data (like combustion) is highly unstable
  Their Solution: A novel global min-max normalization of the entire state vector (species and temperature) to regularize the network .
My Project:
  This project applies the robust data-driven framework from Bansude et al. to the more complex 31-species ammonia mechanism (they used a 9-species H2 mechanism).

## Slide 6
Studio Shodwe
B
05
1
METHODOLOGY
Data Generation
  Tool: Cantera (Python)
  Mechanism: Stagni (2023) - 31 species, 203 reactions
  System: 0D, constant-pressure (1 atm) autoignition
  Parameter Space: Generated 100 simulations by varying T0 [1000-1500K] and phi [0.6-1.4].
Data Pre-processing
The Bansude et al. Method:
  1. Normalization: Found the global min/max for all 32 state variables (31 species + T) across the entire dataset. Scaled all data to [0, 1]. This is the key to stable training.
  2. Interpolation: Interpolated all 100 trajectories onto a standard, 50-point log-spaced time grid to create uniform batches.
2

## Slide 7
3. MODEL TRAINING
06
The "Physics-Informed" Structure:
  We do not learn the state. We train a network (ChemNet) to learn the governing physics (the derivative): du/dt = Net(u, theta)
Model Architecture (model_training.ipynb)
  ChemNet: A 4-layer MLP with 256 hidden neurons and ELU activation.
  NeuralODE Wrapper: This class (from torchdiffeq) takes the ChemNet as its derivative function.
Training Process:
  Solver: odeint integrates ChemNet using a fast, explicit solver (dopri5).
  Loss: Mean Absolute Error (MAE) between the integrated solution (u) and the ground truth.
  Backprop: Adjoint Sensitivity Method.
  Optimizer: Adam with a ReduceLROnPlateau scheduler.
  Epochs: 2500

## Slide 8
4. MODEL EVALUATION
07
The trained model was evaluated on unseen test cases not included in the training set.
Test Case 1: Hot Initial Temp/Lean Mixture
Test Case 2: Warm Initial Temp/Lean Mixture
Test Case 3: Warm Initial Temp/Rich Mixture

## Slide 9
08
CONCLUSION & FUTURE WORK
Conclusion:
  Successfully developed and trained a ChemNODE surrogate for the complex 31-species Stagni (2023) ammonia mechanism.
  The model is highly accurate, with low error in predicting ignition delay and peak radical concentrations on unseen test cases.
Limitations:
  Model is 0D (no spatial effects) and trained for a single pressure (1 atm).
  The model is not providing the required computational speed-up that we wanted in the beginning. (I’m still working on it)
Future Scope of Work:
  Generalize: Include Pressure (P) as an input to the network.
  Add Physics (PINN): Enforce physical constraints (e.g., mass conservation, sum(dY_k/dt = 0) directly in the loss function.
  Couple: Integrate this fast 0D surrogate into a 2D/3D CFD code (e.g., OpenFOAM) to accelerate a full reacting flow simulation.

## Slide 10
09
REFERENCES
Introduction to Neural ODEs
1. Chen, R. T. Q., Rubanova, Y., Bettencourt, J., & Duvenaud, D. (2018). Neural Ordinary Differential Equations. NeurIPS.
2. Owoyele, O., & Pal, P. (2022). ChemNODE: A Neural Ordinary Differential Equations Framework for Efficient Chemical Kinetic Solvers. Energy and AI.
Introduction to ChemNODEs
  Bansude, S., Pal, P., & Bhattacharya, S. (2023). A data-driven framework for integration of chemical kinetics using neural ordinary differential equations. Combustion and Flame.
Reduced Order Reaction Mechanism for Ammonia Combustion
  Stagni, A., et al. (2023). Low- and intermediate-temperature ammonia/hydrogen oxidation in a flow reactor. Chemical Engineering Journal.

## Slide 11
THANK YOU
ANY QUESTIONS?